DaRo UV Systems

# The UV Buddy

### DaRo UV systems are specialists in ultraviolet disinfection and have been manufacturing systems in the UK for over 25 years. Our products are market leaders and approved by health specialists for domestic use. All of our systems are WRAS (Water regulation advisory service) approved.

Our unrivalled design and manufacturing capability allows us to provide a comprehensive standard range of UV products. It also gives us the flexibility to build bespoke UV equipment to our customer's precise requirements. With water disinfection systems ranging from small OEM units through to large industrial systems, our in-house manufacturing enables customised solutions to be offered and backed by our design expertise.

The easy way to retrofit your existing system with the following telemetry:

- Audio visual UV lamp failure alarm

- Lamp lifetime (status) indicator

- Volt Free Contacts

Do you have an existing UV system that you now need to add lamp failure Indicators, Lamp status or even a solenoid valve to stop the water flow in the event of a lamp failure? If so then the DaRo UV systems UV buddy is the system that you will need.

The UV Buddy is a system that allows you to connect your existing UV unit. The system will give you the added telemetry required. The system will give you an audio and visual lamp failure indicator (LFI), lamp status. Volt free contacts are available for remote operation. Allowing connection to a remote buzzer, beacon, solenoid shut off valve, link to Building Management System (BMS), etc. etc. etc.)

The UV Buddy is designed so that it is simply plugged in between the mains supply and the UV system itself.

The UV Buddy is designed to not only work with DaRo UV systems units, but also with other manufacturers UV systems*

The simple plug and play installation of the UV Buddy is the major advantage of the system. With no wiring to do, the unit can simply be plugged in to your existing UV unit.

*System make/model to be specified at point of order

### The specialists in ultra violet light

T: 01787 370187 | www.darouv.co.uk

## Choosing your system

Telemetry: Lamp Failure Indicator (LFI)

The Lamp Failure indicator provides a warning to the user if the UV lamp fails electrically, by activation of a red lamp fail indicator and a sounder. This is linked to a volt-free contact giving provision for a remote warning device to be fitted (see below).

Telemetry: Lamp status indicator

The three-way indicator display showing the status of the system

Audible alarm to warn of lamp failure & end of lamp life. (Can be temporarily silenced.)

Telemetry: Volt Free Contacts (VFC)

The UV Buddy comes with a Volt Free contact (VFC) output, which allows you to connect to a remote device of your choosing for lamp failure indication. The UV Buddy comes complete with a socket so that you can connect the cable to device or shut off valve of your preference.

Specifications

| Enclosure Material | Powder coated steel |
| --- | --- |
| Power Supply | 110 - 240V, 50 - 60Hz Single Phase |
| Plug side fuse | External 13A HBC |
| Socket side fuse | Internal 3A HBC |
| IEC plug to 13A socket | 0.5m long |
| IEC socket to 3A plug | 2m long |
| Volt free contact rating | 3A @ 240VAC max, 0.5A @ 24VDC max. |

The following table gives performance details on the domestic range. To choose the correct unit simply match the application against the unit required. If in doubt, please contact your local stockist or our head office

ECO 1	ECO 2	ECO 3	ECO 5

Chamber construction	316L stainless steel

Control panel construction	304 stainless steel

Typical application (approx.)	Up to 2 taps	Whole house	Multiple user	Multiple user

(small dwelling) (family home)	(guest house)	(Hotel)

Do

Pr

mestic Flow rate		8 litres		19 litres		36 litres		51 litres per minute	per minute	per minute	per minute

La

essure ratings	10 bar working pressure

UV

mp life	8760 hours (1 years continuous use)

lamp	GER15	GER30	GER55	GER55

Co

Di

nnections	¾ inch BSP male thread		1 inch BSP male thread

Po

mensions	See general arrangement drawing for details

Po

wer consumption	28 Watts	38 Watts	75 Watts	95 Watts wer supply			240v 50Hz single phase

*flow based on 98% UV transmission per 1cm at end of lamp life giving a UV dose of 40mJ/cm²

## Filtration

It is important that sediment in the water does not obstruct the UV light. We strongly advise that a 5- micron sediment pre filter is fitted before the chamber to remove contamination. DaRo UV systems have an extensive range of compatible filter units in stock to match the UV chambers capacity. We will be pleased to advise when choosing a unit and propose corrective measures for other water problems

## r

Ro

nd

La

Da

sta

ger units

manuf

specifi

UV Systems can offer a range of larger ard units. Our expertise in design and acture enables us to tailor systems to

c site situations. The systems that we

have manufactured are in regular use in a wide range of applications, from vending machines to municipal drinking water treatment.

## Standard features

- 5 year warranty**

- UK manufactured

- Low carbon footprint

- Robust design

- Low running cost

- Long life / High Reliability UV Lamp

- Maximum 10 bar working Pressure

- Simple to Install and Service

- Polished Chamber

- Commonplace UV Lamps

### The specialists in ultra violet light

T: 01787 370187 | E: info@darouv.co.uk | W: www.darouv.co.uk

Data sheets: DaRo UV Systems strive to keep abreast of new developments in disinfection. Further datasheet information on specific applications is available; please contact us for more details.